## Slide 1
Detection and Robotic Manipulation of Partially Occluded Object(s)
Detecting partially occluded cylindrical objects for robotic manipulation: a multi-method comparison in 3D point clouds
Master's thesis · evaluation review
[FILL: presenter] · supervisor: [FILL: supervisor] · [FILL: date]

## Slide 2
The bin-picking problem
Before the robot can grasp anything, it must know exactly where each object is and how it lies.
Detection and Robotic Manipulation of Partially Occluded Object(s)
1

## Slide 3
Our task: fit a cylinder to the visible points
“Fitting” = choosing model parameters so the model matches the measured points as well as possible
With a full view, fitting is easy — the difficulty starts when most of the object is hidden.
Detection and Robotic Manipulation of Partially Occluded Object(s)
2

## Slide 4
Our case is harder: the drums are covered
Real scan: 200-litre steel drums, tumbled and partially buried
• Drums lie in arbitrary directions.
• Sand and other drums hide most of each drum.
• The sensor sees the pile from one side only.
Each drum shows only a small patch — and a small patch fits many different cylinders.
Detection and Robotic Manipulation of Partially Occluded Object(s)
3

## Slide 5
Existing solutions — three families of methods
From an 18-method literature survey; judged by how they cope with hidden objects
Geometry-based
Search the 3D points directly for cylinder shapes.
+ Works out of the box — no training data needed.
− Needs enough visible points; touching drums get merged.
Learning-based
A neural network learns what partial barrels look like from many examples.
+ Can recognise a barrel from a small fragment.
− Needs lots of labelled training examples first.
Camera + LiDAR
Combine colour images with the 3D points.
+ If one sensor is blocked, the other still sees the object.
− Both sensors must be aligned precisely — errors break the pairing.
We compare all three families on the same data — geometry first, since it needs no training data.
Detection and Robotic Manipulation of Partially Occluded Object(s)
4

## Slide 6
The data we test every method on
Three data sets — difficulty increases left to right
Synthetic clouds tell us the best case; the real pile tells us the truth.
Detection and Robotic Manipulation of Partially Occluded Object(s)
5

## Slide 7
Four geometry-based methods implemented
• 3DTK Hough (baseline) — every point votes for the cylinders it could lie on; the strongest vote wins.
• RANSAC fit — try many random small point samples, keep the cylinder most points agree with.
• Least-squares fit — start from a rough guess, then adjust the cylinder until it matches the points best.
• Efficient RANSAC — a faster RANSAC variant that searches the whole scene for shapes in one pass.
All four: LiDAR points only · no training data · identical input and output — directly comparable.
Detection and Robotic Manipulation of Partially Occluded Object(s)
6

## Slide 8
How we evaluate — one pipeline for every method
A prediction counts as correct if direction is within 30° and the centre within 10 cm of the true drum.
Detection and Robotic Manipulation of Partially Occluded Object(s)
7

## Slide 9
Experiment 1 — how much noise can each method take?
The synthetic barrel (120° visible) at 11 noise levels × 3 repeats = 33 test clouds
• RANSAC and least-squares find the barrel at every noise level (F1 = 1.00 / 1.00).
• Efficient RANSAC degrades first; the Hough baseline is erratic — it even misses some clean scenes.
• Least-squares is the most precise but ~5–10× slower than the others (~17 s per scene).
Detection and Robotic Manipulation of Partially Occluded Object(s)
8

## Slide 10
Experiment 2 — the real lab barrel, no occlusion
Depth-camera scan; true radius 4.25 cm
Camera points (coloured) with the fitted cylinder (red)
Method | Barrel found? | Radius error | Direction error
RANSAC fit | yes | 0.38 cm | 1.9°
Least-squares | yes | 0.47 cm | 1.6°
Efficient RANSAC | yes | 0.94 cm | 0.1°
3DTK Hough | yes + 1 false alarm | 0.09 cm | 1.5°
• All four methods find the barrel.
• Errors are ~6–8× larger than on synthetic data — real sensor noise is not the clean noise we simulate.
Detection and Robotic Manipulation of Partially Occluded Object(s)
9

## Slide 11
Experiment 3 — a real occluded drum from the pile
One tilted, half-buried 200 L drum cut out of the survey scan
True drum (green) vs fitted cylinders on the real points
• All four methods fail the accuracy gate here.
• Best attempt (least-squares): direction good (17°), centre off by 11.1 cm — misses the 10 cm gate by 1.1 cm.
• The others: direction far off, or no detection at all.
Occlusion is exactly where the classical methods break — motivating a learned method.
Detection and Robotic Manipulation of Partially Occluded Object(s)
10

## Slide 12
New: BarrelNet — our first learning-based method
A neural network that gets the points of ONE drum and outputs its pose (centre + direction)
Examples of the synthetic training patches: simulated LiDAR points (red) on the drum surface (blue)
• Trained on 12,000 such patches — buried, tilted, noisy, incomplete.
No real data in training: the 21 hand-verified real drums are kept aside as an honest test.
Detection and Robotic Manipulation of Partially Occluded Object(s)
11

## Slide 13
BarrelNet — how the score develops during training
Same network trained twice: laptop CPU (stopped early) vs GPU server (full schedule)
• Finishing the full training schedule nearly doubled the score: 7 → 12 of 21 real drums.
• The direction is learned early; the centre position improves late — it crosses the 10 cm gate only near the end.
Detection and Robotic Manipulation of Partially Occluded Object(s)
12

## Slide 14
BarrelNet on the real drum pile
Trained purely on synthetic drums, tested on the 21 real ones
Annotated drums coloured; predicted cylinders: green = within gate, red = miss
• 12 of 21 real drums located within the accuracy gate.
• Direction right on 16 of 21 drums.
• The geometric methods scored 0 on this kind of drum.
• Open point: BarrelNet estimates the pose of a drum it is given — finding the drums in the pile still needs a separate first step.
Detection and Robotic Manipulation of Partially Occluded Object(s)
13

## Slide 15
What limits the evaluation today
• Our synthetic scenes still cannot imitate a truly buried, cluttered pile.
• Real sensor noise is harder than anything we simulate — Experiment 2 showed 6–8× larger errors.
• Only 21 real drums are labelled (~30% of the pile) — too few for strong statistics.
• Some labels are imperfect: two drums lying end-to-end were annotated as one.
The evaluation machinery works — what is missing is more and better ground-truth data.
Detection and Robotic Manipulation of Partially Occluded Object(s)
14

## Slide 16
Open risks — and how we deal with them
Risk | How we deal with it
Accuracy collapses under occlusion | Measure it per method — that comparison IS the thesis.
One sensor alone may not be enough | Add camera + LiDAR fusion — it degrades far more gracefully.
Sim-trained models may not transfer | Measured: 12 of 21 real drums; next, fine-tune on a few real ones.
Manipulation not started yet | Detection delivers exactly the pose a grasp planner needs.
Occlusion numbers: [Shi'19] arXiv:1812.04244 · [Kumar'25] arXiv:2511.04347 · [Wang'25] Sensors 25(9):2794
Detection and Robotic Manipulation of Partially Occluded Object(s)
15

## Slide 17
Next step: simulation closes the data gap
NVIDIA Isaac Sim gives unlimited scenes with perfect ground truth
• Every simulated drum comes with its exact pose and its exact degree of burial — labels for free.
• That enables the headline experiment: detection quality as a function of how much of the drum is hidden.
• And it unlocks the remaining families: more learned methods and camera + LiDAR fusion.
Detection and Robotic Manipulation of Partially Occluded Object(s)
16

## Slide 18
Summary
• One fair evaluation pipeline — every method, same data, same score.
• Four geometry-based methods work well on visible barrels — and all fail on a truly occluded one.
• BarrelNet, trained only on synthetic drums, already finds 12 of 21 real occluded drums.
• Next: simulation-generated data for the occlusion sweep, fine-tuning, and sensor fusion.
Learned + simulated is the promising path for occluded drums — and we can now measure exactly how promising.
Detection and Robotic Manipulation of Partially Occluded Object(s)
17

## Slide 19
Thank you!
Questions?